## Slide 1: Numericals on Belt Drives

## Slide 2
A motor running at 1750 rpm drives a line shaft at 800 rpm. If the diameter of the pulley on the motor shaft is 160 mm, find that of the pulley on the line shaft.
Solution:
Data: Driving System: N1 = 1750 rpm, d1 = 160 mm
Driven System: N2 = 800 rpm, d2 = ?
Velocity Ratio = N1/N2 = d2/d1
1750 / 800 = d2 / 160
d2 = 160 x 1750 / 800
d2 = 350 mm

## Slide 3
The sum of the diameters of two pulleys A and B connected by a belt is 900 mm. If they run at 700 and 1400 rpm respectively, determine the diameter of each pulley.
Solution:
dA + dB = 900 mm , NA = 700 rpm , NB = 1400 rpm
Velocity ratio = NA / NB = dB / dA
700 / 1400 = dB / dA
Therefore dA = 2 dB
2 dB + dB = 900
3 dB = 900
dB = 300 mm
and dA = 600 mm

## Slide 4
In an open belt drive running in the clockwise direction, the tension in the tight side is 3000 N and the arc of contact is 1500. If the coefficient of friction is 0.3. Find the tension on the slack side of the belt.
Solution:
T1 = 3000 N, µ = 0.3 , θ = 150o = 150 x Π / 180 radians
T1 / T2 = e µ θ
3000 / T2 = e (0.3 x 150 x Π / 180 )
3000 / T2 = 2.193
Therefore T2 = 1367.9 N

## Slide 5
In a belt drive, the angle of lap on the driven pulley is 1600 and the coefficient of friction between the pulley and belt material is 0.28. If the width of belt is 200 mm and the maximum tension in the belt is not to exceed 50 N per mm width, find the initial tension in the belt drive.
Solution: T1 = 50 N / mm width, µ = 0.28 , θ = 160o = 160 x Π / 180 radians
Width of belt = 200 mm, T1 = 50 N/mm width x 200 mm = 10000 N
T1 / T2 = e µ θ
T1 / T2 = e 0.28 x 160 x Π / 180
T1 / T2 = 2.187
Therefore T2 = 10000 / 2.187 = 4572.4 N
Initial Tension = T0 = (T1 + T2) / 2 = (10000 + 4572.4)/2
Therefore T0 = 7586.2 N

## Slide 6
The driven pulley of 400 mm diameter of a belt drive runs at 200 rpm. The angle of lap is 1650 and the coefficient of friction between the pulley and belt material is 0.25. Find the power transmitted if the initial tension is not to exceed 10kN.
Solution:
N1 = 200 rpm , T0 = 10 kN, θ = 165o , µ = 0.25 , Power, P = ?
T1 / T2 = e µ θ
T1 / T2 = e 0.25 x 165 x Π / 180
T1 / T2 = 2.054
Initial Tension = T0 = (T1 + T2) / 2
Therefore , (T1 + T2) = 2 T0 = 2 x 10000 = 20000 N
2.054 T2 + T2 = 20000
3.054 T2 = 20000
T2 = 20000 / 3.054 = 6548.8 N
and Therefore T1 = 2.054 x 6548.8 = 13451.2 N

## Slide 7
Now, to calculate Power, we have
Power, P = (T1 – T2) v / (60 x 1000)
Belt speed v = Π dN
v = Π x 0.4 x 200
v = 251.32 m / min
Therefore , P = (13451.2 – 6548.8 ) x 251.32 / 60000
Power, P = 28.91 kW